## Slide 1
软硬协同构筑统一异构 KVCache 存储池，达成集群级复用与高效治理目标
KV 语义驱动｜统一异构介质治理｜牵引芯片、网络与存储协同演进
业务层
RAG 公共前缀
多轮智能体
长上下文推理
P/D 分离
推理框架层
vLLM
SGLang
其他推理框架
统一异构 KVCache 存储池｜核心技术分层
L1/L2
框架适配层
vLLM Connector
SGLang Connector
其他框架适配
L3 核心
管理层
元数据直访
QueryPlan
KV传输编排
L4 多态硬件
使能层
多介质治理
全链路QoS
内存语义
UBMEM
传输引擎
URMA
DPU / 网卡 QoS
分层存储 I/O
在线推理相关中间件
框架运行 / 模型执行
计算加速 / 并行通信
传输 / 存储访问
OS／驱动层
芯片/SoC
Runtime
内存映射
一致性
DPU/NIC
驱动
存储I/O
NVMe
异构硬件层
NPU/SoC
HBM
CPU/DDR
C2C
DPU/NIC
网络
NVMe SSD
存储控制
彩色：项目核心覆盖｜灰色：在线推理生态参照
Ray
MP
PyTorch
图编译
权重加载
Adapter管理
FlashAttention
Triton
HCCL
NCCL
通用缓存
对象访问
NIXL
UCX
libfabric
SPDK
io_uring
gRPC / 消息通信
关键竞争力
01
跨框架、跨节点统一匹配与复用，可消费命中率提升 ≥20%、P99 TTFT 降低 ≥20%。
02
芯片—内存—网络—存储全栈协同，HBM 有效容量提升 ≥30%、后台治理引起的 P99 TPOT 劣化 ≤3%。
关键技术
T1
基于内存语义直达前缀目录、block_table 与对象状态，缩短热点元数据访问和一致性发布链路。
T2
KVObject—ExtentManifest 统一表达 HBM、DDR、远端内存与 SSD 的位置、版本和生命周期，实现跨介质一致治理。
T3
面向 KV 业务意图编排元数据查询、前台拉取、Store 入库和后台迁移，贯通队列、链路与存储 QoS，保护 TTFT/TPOT。
T4
QueryPlan/Descriptor 将 KV 收益决策编译为芯片、SoC、DPU/网卡、网络与存储动作，形成牵引硬件演进的全栈闭环。
Notes: [Sources]
Local project architecture:
D:\codes\reports\kvcache\unified_kv_memory\统一异构KVCache存储池总体架构与SRS评审导读_定版.md
D:\codes\reports\kvcache\unified_kv_memory\outputs\需求基线复核_20260717\统一异构KVCache存储池总体架构与SRS评审导读_V2.2_传输底座视角_建议修订版.md
D:\codes\reports\kvcache\unified_kv_memory\竞争力总结\统一异构KVCache存储池_关键技术与竞争力_讨论稿.md
Mooncake primary references:
https://github.com/kvcache-ai/Mooncake/blob/main/docs/source/design/mooncake-store.md
https://kvcache-ai.github.io/Mooncake/design/transfer-engine/index.html
https://kvcache-ai.github.io/Mooncake/design/tent/transport-selector.html
Comparison note:
Mooncake already provides object-level KV storage, zero-copy and multi-NIC transfer, multiple transport backends, RAM/SSD tiering, and request priority in TENT. The visible slide therefore avoids generic feature-parity claims. It emphasizes this project's intended differentiation: memory-semantic direct access to hot metadata; KVObject/ExtentManifest lifecycle semantics across heterogeneous media; KV-intent QoS across metadata, foreground fetch, store ingress, and background governance; and QueryPlan/Descriptor compilation into chip, SoC, DPU/NIC, network, and storage actions.
[/Sources]